## Slide 1: Connecting Ammeters and Voltmeters in a Circuit

## Slide 2: Connecting the Voltmeter
Voltmeters are connected in parallel.
  This means that they are connected across the device.
R1
R2
+
V
R3
V
V
V
A voltmeter is a peripheral device that does not affect the operation of the circuit itself.

## Slide 3: Connecting the ammeter
R1
R2
+
V
R3
While voltmeters are connected in parallel, Ammeters are connecting in series.
  This means that they are an integral part of the circuit.
  Current has to flow through them in order for them to take a measurement.
A
A
I
Am
Serious
Remember:
Current
Ammeter
Connect in Series

## Slide 4: Example: Which one(s) is (are) correct?
Ammeters in series (1), and Voltmeters in parallel (4)
1
2
3
4

## Slide 5: Example Where to place the meter
What type of circuit is it?
Where would you put a meter in the circuit to measure the total current?
Where would you put a meter in the circuit to measure the current through R1?
Where would you put a meter in the circuit to measure the current through R2?
Where would you put a meter in the circuit to measure the total voltage?
1
2
3
4
Parallel
AT
A1
A2
V

## Slide 6: What does happen when a meter is connected incorrectly
REMEMBER: ELECTRICITY ALWAYS TAKES THE PATH OF LEAST RESISTANCE
What happens if an ammeter is connected in parallel?
  You get a short circuit. Why?
  Because ammeters have virtually no resistance.
What happens if a voltmeter is connected in series?
  The circuit will not operate. No current will flow. Why?
  Because voltmeters have virtually infinite resistance.

## Slide 7: PHET Simulation