## Slide 1: Power & Electrical Energy

## Slide 2: What is Electrical Power?
Where do we get the electricity that powers our homes and businesses on a daily basis, 24/7?

## Slide 3: Power
Power = Rate at which work is done where:
    P = 1 Joule/second = 1 Watt
    P = VI = (1 Volt)•(1 Ampere) = 1 Watt
V = W/q = 1 Joule/Coulomb
I = q/t = 1 Coulomb/second
Since and :

## Slide 4: Example (Power)
What is the power rating of a lightbulb in circuit where the current is 0.50 A and the voltage is 120V?

## Slide 5: Power vs. Current and Power vs. Voltage (Ohmic Materials)
What is the relationship between:
  power and current? Power and voltage?
Current
Power
Voltage
Power
The resistance is constant for Ohmic materials.

## Slide 6: Energy
Since power is the rate at which work is done the amount of energy required to complete a task is as follows:
Total Energy = Power x time
Recall that and

## Slide 7: Example (Energy)
How much energy is consumed by a lightbulb operating in circuit where the current is 0.50 A and the voltage is 120V for 1 hour?